ARM architectures
https://en.wikipedia.org/wiki/List_of_ARM_processors
Assembly language tutorials:
https://azeria-labs.com/writing-arm-assembly-part-1/
https://developer.arm.com/documentation/dui0473/m/writing-arm-assembly-language?lang=en
GNU Assembler:
https://developer.arm.com/documentation/den0013/d/Introduction-to-Assembly-Language/Introduction-to-the-GNU-Assembler
ARM/Thumb/ThumbEE processor instr. set modes:
https://developer.arm.com/documentation/dui0473/m/overview-of-the-arm-architecture/changing-between-arm--thumb--and-thumbee-state
Processor modes(privilaged or not):
https://developer.arm.com/documentation/dui0473/m/overview-of-the-arm-architecture/processor-modes--and-privileged-and-unprivileged-software-execution
Extra registers for processor modes.
https://developer.arm.com/documentation/dui0473/m/overview-of-the-arm-architecture/arm-registers
Register names
https://developer.arm.com/documentation/dui0473/m/overview-of-the-arm-architecture/predeclared-core-register-names
GNU GCC options
https://gcc.gnu.org/onlinedocs/gcc/ARM-Options.html

Thumb-2 is still Thumb

https://community.silabs.com/s/article/understand-the-gnu-assembler-startup-file-of-cortex-m4?language=en_US

How to read processor mode & instr. set mode?
How to view Cortex registers in Clion?

Pin in alternative function mode stays tri-state till peripheral is enabled.
Peripheral does not force own push-pull/open-drain config for output.

# Memory types and attributes
Types
Normal – access may be reordered
Device – ‘happens after’ is guaranteed relatively to transactions to Device and Strongly-ordered memories.
Strongly-ordered – ‘happens after’ is guaranteed relatively to all memory types.

Applicable for some advanced cores.
Shareability domain – is part of memory for which read/write sequence is predictable(writes to diff. domains may actually complete in a different order, than in a program).
# Some Cortex Commands
ISB(instruction sync. barrier) – resets prefetch buffer of FLASH, so next instr. will be read again(and new setting of “memory management unit” will be applied to this and next instructions).

DMB(data memory barrier) – all writes(some of them were buffered/cached) before this instr. will be visible to all masters in a system(buffered data is actually flushed to memory) before next data access instruction(execution is not blocked if several next instructions do not access memory).

DSB(data sync. barrier) – similar to DMB, but core is blocked till sync. is completed.

LDREX, STREX – exclusive “load”(closes exclusive monitor) and “store”(opens monitor). STREX stores and returns 0 only if exclusive monitor is “closed”, otherwise – returns 1.

# Useful Cortex registers
PRIMASK – contains flag which disables(if 1) interrupts with configurable priority
FAULTMASK – contains flag which disables all interrupts(yes all) except non-maskable.
CONTROL – shows what stack pointer is used(main/process), defines privilege or thread mode(norm. exec. - not IRQ handler).
BASEPRI – sets min. IRQ prio. which may be served – only strictly more priority may be served. Value 0 – has no effect. Do not forget to shift left value if priorities are 8bit in your system.
IPSR – what is executing now, for example: 0 – Thread mode, … 5 – BusFault handler, … 16 – IRQn handler.
VTOR – address of ISR-vector table(actually offset but relative to 0x0). Spec. says that bit29 indicates, that table in SRAM – don’t care, 1<<29 is a start of SRAM. Value for MSP is also a part of vector-table. About alignment: if N is a size of your vector table(in words), take next M(in words) which is power of 2, your vector-table address should be M-aligned.
SCR(System Control Register) – control of low-power modes
# Cortex stacks
IRQ handlers always use main stack – writes to CONTROL.SPSEL has no effect. Thread may use either main(by default) or process stack - it is not connected with thread privilege mode, priviledge mode allows/restricts writes to some registers and commands.
On IRQ return – hardware sets correct stack for Thread.
Register SP is like alias for MSP or PSP – depending which stack is currently used.
Stack pointer decrements before push – so points to last stored value.

# FPU
https://developer.arm.com/documentation/dui0646/c/Cortex-M7-Peripherals/Floating-Point-Unit
Inexact result – if resulting mantissa has more significant bits, that can be stored.
Underflow – if result is too small for “normalized presentation”(with leading 1).
Quiet vs Signaling NaN – special values, “quiet” just propagates through calculation, signaling – causes exception(traps are not supported in stm32).
Most models don’t have ‘enable irq.’ bits – enable/disable via NVIC.
Flush to zero – feature, which sets result to 0 if it can not be presented as normalized float(with leading 1).
Default NaN – feature, which treats input NaN as Quiet NaN, NaN results will be also Quiet NaN.
Rounding modes – round to nearest/pos. infinity/zero/neg. infinity.
Standard half-precision float – has sign, mantisa and exp. as usually, but has less bits(16). Alternative half precision – denormalized, fixed exponent(16), bit weights(starting from MSB): 1/2, 1/4, 1/8, …
## How to enable
Allow access to FPU by setting CP11, CP10(should be equal) in CPACR.
Set how to push FPU regs. on IRQ(see below) in FPCCR.
Set rounding and other features in FPSCR. Note it is not mapped to memory – access it via VMRS/VMSR instructions or __get_FPSCR()/__set_FPSCR().
Add compiler & link options(yes, the same): -mfloat-abi=hard -mfpu=fpv4-sp-d16
Add compiler defines like(see your CMSIS-DSP): ARM_MATH_CM4;ARM_MATH_MATRIX_CHECK;ARM_MATH_ROUNDING
Compiler defines as __FPU_USED, __SOFTFP__ , __VFP_FP__ are made by compliler depending from -mcpu, -mfloat-abi and -mfpu – do not change that.
You might want to add:
-fsingle-precision-constant – to treat double literals as single precision(not double precision).
And other described here: https://gcc.gnu.org/wiki/FloatingPointMath
and documented here: https://gcc.gnu.org/onlinedocs/gcc/Optimize-Options.html
## Saving context on IRQ
It’s possible to push/pull regs. of FPU(only S0..15, S16… should be saved manually before usage) automatically(by hardware) – set FPCCR.ASPEN.
Not all ISRs may need FPU, so there is “lazy” automatic pushing – enabled by FPCCR.LSPEN. In this case regs.(S0..15) will not be pushed to stack, but space for regs. will be reserved – start of reserved stack address is automatically written to FPCAR. Regs. are actually (automatically) pushed at(right before) first access to FPU. All works automatically for ISR returns and nested IRQs.
Just for info(all works automatically)
CONTROL.FPCA is set to 1 at first FPU access in fresh context: thread accessed FPU for the 1st time or IRQ accessed FPU(will be reset automatically after return) for the 1st time.
FPCCR.LSPACT is reset to 0 after regs. are actually pushed(so should be pop-ed during return).

## CMSIS-DSP lib naming from ST
arm_cortexM4lf_math.lib (Cortex-M4, Little endian, Floating Point Unit)
arm_cortexM4bf_math.lib (Cortex-M4, Big endian, Floating Point Unit)
arm_cortexM4l_math.lib (Cortex-M4, Little endian)
arm_cortexM4b_math.lib (Cortex-M4, Big endian)
# NVIC
Interrupt also becomes pending if interrupt signal is high, and this interrupt is not enabled by NVIC.

# SysTick
24 bit wide. Counts down from SYST_RVR to 0. Does not down-count if halted for debugging.
Interrupt(which may be enabled/disabled) is generated during 1→0 transition(interrupt routine may read 0 if SysTick is sufficiently prescaled).
Any write to CVR(Current value register) – clears this register(and COUNTFLAG in ‘control reg.’).
Registers. CSR – control and status, RVR – reload value, CVR – current value, CALIB – contains value for RVR(and flag that it exists) to get 10ms period.

# PWR
POR – power-on reset, PDR – power-down reset.
BOR – brownout reset; allows to redefine(via option bytes) VDD ranges when device is not in reset.
Optional PDR_ON pin allows to disable internal POR/BOR.
Optional BYPASS_REG pin allows to disable internal regulator.
PVD – programmable(some PWR register) voltage detector; connected to one of EXTI lines so may invoke interrupt if VDD/VDDA are out of desired range.
Enable clock in RCC prior using.

Enabling overdrive:
1) ensure, that sysclock is HSI or HSE.
2) enable overdrive(ODEN) → wait overdrive to be enabled(ODRDY)
3) switch to overdrive(ODSWEN) → wait for switching to be ready(ODSWRDY)

Changing “voltage scale”:
1) ensure that PLL is of
2) change VOS[] → VOSRDY will rise after enabling PLL

## HAL notes
Clear flag of wake-up pin: __HAL_PWR_CLEAR_WAKEUP_FLAG()
# Clock control
If CSS is enabled and external clock fails – non-maskable int. is generated and some timers receive “break” signal. Interrupt should be cleared by writing CSSC in RCC_CIR.
## HAL notes
RCC_OscInitTypeDef::OscillatorType and RCC_ClkInitTypeDef::ClockType are bit-flags to show what settings should be applied/ignored.
# Low power modes
Does SysTick work in sleep?
Sleep mode.
Enter via WFE – wake-up by enabled in NVIC interrupt; if SCR(System Control Reg.).SEVONPEND = 1 – also by interrupt not enabled in NVIC(yes NVIC generates wake-up event, do not forget to clear pending bit); by EXTI line, configured to generate as event.
Enter via WFI – wake-up by enabled in NVIC interrupt.
Enter via ISR return with SCR.SLEEPONEXIT = 1(should be cleared manually) – same as for WFI.
PWR_CR1.PDDS decides Stop or Standby(the deepest).
Stop
Pins stay as during runtime, core & periph. clocks are off(HSE, HSI, PLL are disabled).
More bits in PWR_CR1 to reduce current:
FPDS – flash in power-down.
UDEN – use underdrive both for main & low-power regs.
LPDS – use main reg. or low-power reg.
MRUDS – set with UDEN=underdrive & LPDS=main reg; this puts flash in power-down(ignoring FPDS)
LPUDS – set with UDEN=underdrive & LPDS=low-power reg; this puts flash in power-down(ignoring FPDS)

Enter like in Sleep + SCR.SLEEPDEEP = 1 – exit as from Sleep, but almost all peripherals are off, so EXTI, RTC (maybe IWDG ) are the only options.
After exit: HSI RC – as clock(unexpected clock for peripherals), voltage scale as before entering, overdrive disabled, PLL disabled (did not check HSI)
Standby
Enter like in Stop + PWR_CR1.PDDS = 1 - exit via hard-reset, IWDG reset, WKUPx pins, RTC event.
Wake-up pins are configured by: PWR_CSR2.EWUPx(enable), PWR_CR2.WUPPx(polarity).
Wake-up from RTC configured by: PWR_CSR1.EIWUP(enable)
# EXTI
Pin from what port to use is selected in SYSCFG(enable it’s clock) or AFIO(enable it’s clock)
Clear pending flag by writing 1 in EXTI→PR. Masked(inactive) interrupts in EXTI→IMR do not rise flags in EXTI→PR.
Generate interrupt by software using EXTI→SWIER.
## HAL Notice
Both HAL_GPIO_EXTI_IRQHandler() and HAL_EXTI_IRQHandler() may miss next signal edge.
# SPI
CPOL – SCK in idle. Mode 0..3 = {CPOL.CPHA}
Disabling SPI(SPE=0) while exchange does not immediately stop it – exchange will be finished, check BSY flag.
In bidirectional mode, while transmitting RXNE flag does not rise(and RX FIFO stays empty).
RXNE is rised in 1 SPI clock cycle after dataframe is received.
TXE is rised when TX FIFO level is <=0.5 of it’s capacity.

Motorola mode
NSS encloses each dataframe if capture data on 1-st clock edge(CPHA=0, any CPOL). In bidir. mode, while last byte receiving(SPE is already 0) NSS is released on last bit capturing edge – it’s a bug.
Otherwise NSS is just forced low after SPI is enabled.
MISO of non-selected slave is HiZ.

Some interrupt flags are cleared by reading SR, other by reading sequence??

Notice about HAL driver
SPI is enabled(and pins are driven by SPI) after first HAL_SPI_Transmit/Receive() call.

# Timer
“Prescaler register” is buffered.
“Auto-reload register” is buffered if ARPE=1.
“Repetition counter” is buffered.
In up/down mode update is generated after “counter” equals 0/”auto-reload” again.
In center-aligned mode update is generated when counter equal 0 and “auto-reload”.
Clear interrupt flags in SR by writing 0, except CCxIF – read CCRx or write 0.

## Output capture
Timer controls pins after CCxE is set(even with disabled counter: CEN=0).
“Capture compare register”(CCRx) are preloaded if OCxPE=1(in CCMRx).
CCxE, CCxNE, OCxM (channel enables and mode selector) are preloaded if CCPC=1(in CR2), CCUS(in CR2) defines when new values take effect.

Outputs are configured by
“off-state selection” in run mode(OSSR in BDTR) – push-pull/tri-state if channel in “inactive” state.
“off-state selection” in idle mode(OSSI in BDTR) – push-pull/tri-state if channel in “inactive” state.
“polarity” bits(CCxP in CCER) – channel’s “active” state is 1 or 0(see OSSR above), in run mode.
“idle state” bits(OISx in CR2) – channel’s state in idle mode.
“Idle mode” – when “main output enable”(MOE) = 0, “run mode” – MOE=1.

Break function
There is separate “break input”(may be mapped to pin) with conf. polarity and filtering. It resets MOE(“main output enable”). MOE may be set again automatically if AOE = 1(in BDTR, on next update event if break is not active).
Write to “Break enable”(BKE) and “break polarity”(BKP) takes 2 APBx clocks.
Sometimes break may be enabled only when OSSI=OSSR=1, check datasheet.
It is possible to force OCxREF low by “external trigger” pin – use OCxCE from CCMRx.

## Input compare

Notice about HAL
Output compare channels are driven by timer(and CCxE=1) after first HAL_TIM_OC_Start() call.

# USART
“Idle character” – all 1 including start-bit(yes, line is driven high) opt. parity bit and stop-bits. It is just line, which does not transmit anything. You may detect, that line is idle by checking flag IDLE, interrupt may be invoked if IDLEIE=1. IDLE is set only once during long line idle – after it first detected after some transmission(or receiver enabling).

“Break character” – all 0 including opt. parity bit and stop-bits(yes, line is driven low during stop-bits) + extra 2 valid stop-bits(exactly 2 despite configuration). Receiver treats it as frame error.

Data frame length(M[] in CR1) – also includes optional parity bit(M=00 → length=8 data-bits or 7 data-bits + 1 parity bit).
TXE(TX empty), RXNE(RX not-empty) – trigger interrupt if TXEIE=1, RXNEIE=1 despite of TE(transmitter enable), RE(receiver enable), UE(uart enable).

Half-duplex. Set HDSEL(in CR3) and conf. TX in open-drain(RX not used). If there is something to transmit(in TDR) - TX becomes output and sends, during all other time – it receives.
## Transmitting
UART controls pin after TE=1.
First data transmission after TE=1 starts in 1 idle character.
Disabling TX(TE=0) while transmission corrupts dataframe.
Flag TXE means, that something may be written to TDR(transfer data register), transmission of prev. data frame may be ongoing at this moment(shift reg. still contains something).
Flag TC (transfer completed) rises when both TDR and shift. reg. are empty – all is transferred including stop bits, it’s safe to disable UART now.
## Receiving
In case of 2 stop-bits – duration of 2nd is not checked(can not cause frame error), RXNE is raised after 1st stop-bit.

Receiver may detect, that transmitter stuck by using “receiver timeout” feature. Enable feature by RTOEN=1(in CR2), enable it’s interrupt by RTOIE=1(in CR1), check it’s flag RTOF(in ISR).

Flags
NF(Noise flag) – line is noisy(3 middle samples are not-equal), clear by writing 1 in NFCF(in ICR).
ORE(Over-run flag) – clear by writing 1 in ORECF(in ICR)
FE(Frame error) - something wrong with start/stop bits, clear via ICR.

Notice about HAL
Good enough. There is method to receive till idle char.

# DMA
In mem-to-mem mode – source is SxPAR. Direct mode is forbidden.
SxNDTR(number of transactions from/to peripheral) – indicates how many left.
Disabling DMA(EN=0) is not immediate – will take effect after ongoing transaction. Read EN to check if DMA if actually disabled, “transfer completed” is also raised in this case.

FIFO
4 words length, keeps data to be written to destination.
Periph-to-mem: collects data till threshold → drains to mem.
Mem-to-periph: fully loads at the beginning, if empties till threshold → loads to be full.
Mem-to-mem: loads till threshold(even at the beginning) → drains to destination.

While flushing: if MSIZE is 2bytes but FIFO contains 1byte – still 2 bytes will be written, check SxNDTR to know how many “good” bytes are in buffer.

Direct mode – stream’s FIFO is not used, data width of source and destination should be equal(PSIZE=MSIZE).

If PSIZE != MSIZE→ number of transfers(SxNDTR reg.) means transfers to/from peripheral.
PSIZE, MSIZE, SxNDTR should guaranty that all transfers are complete.

Circular mode – indefinite loop, number of transfers(NDTR) is automatically reloaded at the end. Memory address registers(MxAR’s) never change – so start from the beginning of buffer.

Double-buffer mode – indefinite loop, memory addresses (SxM0AR and SxM1AR) are swapped at the and. You may change currently unused MxAR on the fly(check flag CT if SxCR). May write CT before enabling DMA to define from what buffer to start.

FIFO overrun/underrun error(flags FEIFx – FIFO error, DMEIFx – Direct mode error) does not disable DMA, because request from peripheral is not acknowledged till error disappears.

Status flags are cleared by writing 1 to corresponding “flag clear register”.

Burst transfers
Several un-breakable transactions, may be used independently for perip. and mem. sides.
If transfer 2bytes per transaction, address readen/written in burst must be 2byte aligned, if 4bytes(words) – word aligned.
Addresses readen/written in burst should not cross 1KByte address boundary(should be between 1KB aligned addresses).

# I2C
SDA changes after SCL goes low and samples after SCL goes high(no concept of sampling on edge).

Slave by default. Switch to master after START generation, switches back to slave after STOP or loss of control over bus.
PE=0 – releases pins, resets flags and state-machine.

Clock configuration
Configure separately low/high time(SCLL/SCLH), delay between SDA changes and SCL rising edge(SCLDEL), delay between SCL falling edge and SDA changes(SDADEL). All configs have the same prescaler(PRESC).
SCLL/SCLH count since low/high level detected(+analog filter+digital filter+2..3 periph. clocks)
SCLDEL counts since bit applied to pin, SCL is forced low during this delay.
SDADEL counts since SCL falling edge detected(+analog filter+digital filter+2..3 peripheral clocks), SCL is forced low during this delay.
Max. delay of analog filter – 230ns. It suppresses 50ns spikes.
Digital filt. counts how long(in peripheral clocks) level is stable.

Own slave addresses
Supports 2, both should be enabled by OAxEN.
OA1 – 7/10–bit address (depending from OA1MODE).
OA2 – only 7 bit; [0...7(yes even all)] bits may be masked(not taken into account); 0000xxx and 1111xxx are special addresses – masking will not acknowledge them(put them to OAx to be able to respond).
Check ADDRCODE(in ISR) to know what address was called.
0000000+0 – general call address(write), will be served if GCEN=1.
OA1[7:1] are used for 7-bit addresses, OA1[0] – not used. Same for SADD(slave address) in CR2.

Receiving
Data from shift reg. is copied to RXDR before last ACK/NACK clock. If RXDR is not empty – clock low state is stretched.

Transmitting
Data from TXDR is copied to shift reg. after last ACK/NACK clock. If TXDR is empty – clock is streched.
Writing 1 to TXE(in ISR) clears TXDR.

Flag TXIS – byte was transmitted and ACKed. TXIS does not rise if not ACKed – check flag NACKF.

Byte counter(NBYTES in CR2) is always active in master mode and may be enabled in slave mode by SBC(Slave byte control) = 1 int CR2.
After NBYTES reaches 0 – TC (or TCR) goes high, int. may be invoked and master should decide to STOP or ReSTART.

AUTOEND – incompatible with RELOAD=1 or in slave mode.

## Common
Flag TXIS works like “TX reg. is empty”. 1st rises after address acknowledged, then – after ACKed byte. If TXDR was empty – may stay high till 2 writes are done(if NBYTES >=2 ), because 1st write immediately moves to shift reg. Write to TXDR clears TXIS, state machine keeps it 0 when nothing is needed to transmit - keep corresponding interrupt enabled, it is safe.
Writing 1 to TXIS triggers interrupt or DMA request.

Write to TXE(yes in ISR) – clears TXDR from prev. byte if transmission was stopped by NACK. Without such clearing old data will be transmitted during next transmission.

Flag NACKF rises only on device which expects acknowledge(own NACK is not detectable).

Clear STOPF, NACKF by writing 1 in ICR not to have overruns and other errors.

STOPF is rised on both involved in communication and on not-addressed??

## Master
NBYTES is used both for read and write. Should be configured before(or together with) START.
If slave did not ACK address: NACKF=1, START is still 1 – use it to define phase of communication.
SADD[7:1] are used in 7-bit address mode, SADD[0] is not used.

Typical write. TXIS rises exactly NBYTE times. After all transmitted – rises TC, now set STOP or START(for Repetitive Start). STOPF rises after “stop” is generated.
If something NACKed – does not rise TC, rises NACKF, after clearing it - “stop” is generated automatically. Not possible to generate ReSTART while serving NACKF.
TC is cleared by setting START/STOP.

Typical read. RXNE rises NBYTE times. Last byte is NACKed. After all received – rises TC, and then as for write.

Auto-end feature. As typical write/read but TC never rises - does not give an option for “re-start”, “stop” is always generated instead.

Auto-reload feature. Allows to write/read >= 255bytes(less is also ok). After NBYTES written/read – rises TCR(int. is also enabled by TXIE). Than you config NBYTES and RELOAD and transmission continues – reset RELOAD if it is the last chunk. After the last chunk TC rises.
TCR is cleared by writing non-0 to NBYTEs.
If something NACKed when RELOAD still 1 – TCR does not rise, NACKF rises instead.

## Slave
Typically NBYTES is not used, but will be used if SBC=1(in CR1), see below.

Typical write(to master). Nothing special.

Typical read(from master). Set NACK(in CR2) after last desired byte is received, so next will not be acknowledged. RXDR will still contain NACKed byte, SCL will not be stretched till NACKed byte is read from RXDR. No need to clear NACK(in CR2) – will be cleared after NACK generation/STOP/next address match.
To decide ACK/NACK right after received byte. You may use RELOAD=1 with NBYTES=1 with SBC=1 to set NACK during serving TCR flag(invoked after each byte)(see below about SBC).

Setting SBC=1 may be done while serving flag ADDR(convenient before enabling I2C), requires NOSTRETCH=0.

Typical write(to master) with SBC. Set NBYTES while serving flag ADDR(before clearing). Handler of TXIS will be invoked NBYTES times(or less if master stops reading by NACK). If master reads more than NBYTES – slave sends 0xFF. TC does not rise after NBYTES transfer.
NACKF still rises if master generates it.

Typical read(from master) with SBC. Set NBYTES and RELOAD while serving flag ADDR. Handler of RXNE is invoked NBYTES times, then TCR rises. While serving TCR set NACK, some non-0 to NBYTES(to clear TCR), optionally clear RELOAD – this generates NACK right after current (NBYTES-th) byte. TC does not rise after NBYTES read.

## HAL notes
Use this shit only as master.

No need to enable I2C after HAL_I2C_Init().

Defining own address(for OA1) and slave address(for SADD while read/write) shift them 1 bit left in 7-bit addressing.

If HAL_I2C_Slave_Transmit_IT() with more bytes, than was actually read → NACK error for slave, + not sent data is ignored(invoke *_Transmit_IT() again).
If HAL_I2C_Slave_Transmit_IT() with less bytes, than master wants to read → communication stucks continuesly reentering ISR with SCL pulled low.
If ..._Slave_Receive_IT(.., for example 3 bytes) and ...Master_Transmit_IT(.., 4 bytes - 1 byte more) – it will be received 4 bytes(yes, with buffer overflow) and all ...Cplt...() calbacks are invoked as for normal transaction.
If ...Slave_Receive_IT(..., for example 3 bytes) and ...Master_Transmit_IT(…, 5 bytes – at least 2 bytes more) – communication stucks – slave holds SCL low and continuesly reenters ISR.

HAL_I2C_GetError() returns HAL_I2C_ERROR_***
# DAC
EN bit enables analog part, digital interface works even with EN=0.
Resolution of sample is defined by register it is written to.
Actual conversion starts on trigger, DMA request is also sent on trigger – write 1st sample your self(if it is valuable).

# ADC
Time for conversion is: {configurable sampling time} + 12.5 clocks; if trigger is external – add APBx period.
ADCON=1 wakes-up from ‘power down’(write 1 when ADCON is 0).
Set ADCON again (after start-up delay) – works as ‘software trigger’ for ‘regular channels’(SWSTART).
But, making CR2 |= JSWSTART / RSTCAL / CAL / CONT / etc. (which actually writes ADCON=1) work as software trigger, reset of calibration, … - regular conversion will not be triggered.
So making only CR2 = CR2 while ADCON=1 triggers conversion.

Resetting ADCON – power-downs ADC immediately – ongoing conversion will not rise EOC.

EOC rises even for injected conversions(together with JEOC).

Changes of ADC_SQRx/_JSQRx during conversion – restarts conversion of modified group.

JSQx with 1st conv. depends from JL:
if JL=0 → conv. channel from JSQ4; if JL=1 → conv. channels from JSQ3, JSQ4; etc.
JDRx does not depend from JL: JDR1 - 1st conv., JDR2 - 2nd conv, ...

SCAN=1 – means convert whole group(not just 1st channel), EOC/JEOC are 1 only after whole group converted. ‘regular group’ shares the same DR – use DMA to store values of individual ‘reg. ch.’.
Writing 0 while ongoing conversion is not documented. Checked experimentally:
- regular conversions are completed with EOC after each
- current injected conversion ends with EOC but without JEOC, next conversions do not start

CONT=1 – means auto start conversion after current is ready. If SCAN=1 – starts conv. of whole group. Does not work for ‘injected conversion’. What happens on write 0?

JAUTO=1 – means convert ‘injected channel’ after regular is done. End of ‘reg. conv.’ works like trigger of injected – other triggers of ‘injected conv.’ should be disabled.
EOC rises after regular group. EOC & JEOC rise after injected group, SCAN=1 does not change this.
What happens on write 0?

DISCEN=1 or JDISCEN=1 (only 1 should be set) – trigger starts conv. of a part of group, length of the part is defined by DISCNUM[..] or JDISCNUM[..].
Example: all group is (1, 2, 3), part length is 2, then on each trigger: (1, 2)→(3!)→(1, 2)→(3)…
Note: EOC is set after individual channel conv.(NOT after all part). Check this!
Note: EOC & JEOC are set after all injected channels are scanned. Check this!

Triggers. Have ‘enable bit’ and ‘trigger select. bits’. Software trigger also belongs to external triggers.

Analog watchdogs.
Regular and injected channels share the same thresholds.
Separate ‘enable bits’ for regular and inj. channels.
Applicable to all channels in group or 1 selected channel(AWDSGL=1, and AWDCH[..] - may be regular or injected)

Calibration. Set CAL and wait till it is reset by hardware. Calibration value is available in DR and is stored in internal registers. To reset calibration write RSTCAL=1 and wait till it is cleared by hardware.

There is a flag which indicates, that conversion started(should be cleaned by sw).

# SDIO
SD I/O – is some periph. which communicates over SD bus and protocol.

Bus in Idle state in 8 clocks after command and data paths are in idle state.
8 clocks is a min. delay between host commands or host command and card response – helps to distinguish packets. State machine cares about there delays it self.

“Command ID” from response is stored in RESPCMD. Info from response - in RESP1..4 registers(32 bits each); actually short responses(48 bits, like R1) have 32bits of data → RESP1, long (136bits, like R2) have 128 bits → RESP1..4.
All short responses have CRC7 field(all 1 even for R3) – SDIO checks CRC for all command.
The only long response is R2, contains CID/CSD with own CRCs – SDIO calculates CRC only for CID/CSD and compares it with their own CRCs, take CRC flag into account.
Timeout for command response is fixed and is 64 clocks.

Flag STA_CMDSENT rises after command is sent and response is not expected.
Flag STA_CMDACT is set and cleared by hardware – shows when command exchange is active.

Int. and pend flags in cmd. register? On PendCmd from data path, state machine goes to ‘send’

Commands are 48bit long(6 bytes) including CRC7. Command path operates in half-duplex. CMD pin is Hi-Z except when state mach. is in ‘send state’.

Command response may be 48bit(6 bytes) or 136bit(17 bytes) long including CRC7. Some responses do not have CRC – ignore CCRCFAIL flag.

Data state machine moves to send(Wait_S, Send) or receive(Wait_R, Receive) states after write to data ctrl. reg.
Returns back to idle state from receive states after
- all data is read(byte counter is 0 and FIFO is empty)
- after timeout
- if FIFO overruns
- CRC check fails

Returns back to idle from send states after FIFO under run. After all data is sent(byte counter is 0) - moves to busy state(and then to idle, if CRC check passed).

Busy state means wait SD card to calculate CRC.
If card reports failed check – move to idle. If no report during timeout – move to idle. If check is ok – return to idle.

Timeout for data (in reg. DTIMER) starts when data state machine is in R_Wait or Busy.

Data FIFO is 32 words(32bit) = 128 bytes.

Start bit error interrupt enable?

HW flow control – allows to stop clock to prevent FIFO over/under run(allowed by SD spec., some MCUs have bug here)

CMD55(APP_CMD) – means that next command is not regular command but application specific command. Card status(in R1 response to next command) has APP_CMD=1 – means, that command was recognized as application specific.

CMD22() - used to address UC cards, it should be executed before read/write single/multiple block and it contains 6 MSB bits of address.

CMD12 recovers from ADDRESS_ERROR
## Pins
Desired to have all pins except SCK pulled-up because they are in input state for significant amount of time.
DAT0 – also works as “busy signal”, active low (SD may need some time to process some commands – defined in spec.)
DAT1 – also “interrupt signal” for SD I/O, active low.
DAT2 – also “read wait signal” for SD I/O, active low
DAT3 – also “card detect signal”, has enabled 50k pull-up, so host detects that DAT3 became high. Pull-up may be disabled by ACMD42. Also “chip select” in SPI mode.

To enter SPI mode – send CMD0 with DAT3(chip select) = 0.

## Simplified phy. layer spec. pages
41(70) – identification procedure(contains 2nd figure with more details)
50(76) – figures for data-transfer mode
102(128) – command-arguments(shortly)-response table
117(143) – response formats
120(146) – card status bits(as in R1 response)
125(151) - SD Status bits
222(248) – Card registers
188(214) – How to work with UC cards

## Identification process
After card is inserted, wait max(1ms, 74 clocks) before first command(CMD0).
In identification mode SDIO_CK speed if 400kHz max. After initialization may be changed on the go.

## “Data transfer mode” state diagram

## Card registers
OCR (operation conditions reg.) - supported VDD window, flag that power up proc. completed, flag that shows if card is SC or HC/XC.

CID (card ID) – unique ID of card(has manufacturer, manufactured date, etc.) 128 bits, but bit 0 is always 0. Also contains own CRC7.

CSD (card specific data) – structure depends from card type (SC/HC/XC), mutable part is changed via CMD27. 128Bits, but bit 0 is 1. Also contains own CRC7. Most interesting:
- CSD_STRUCTURE – card type SC or HC/XC or UC(ultra capacity)
- DSR_IMPL – if DSR reg.(see below) is implemented.
- C_SIZE – card capacity, for HC/XC = (C_SIZE + 1) * 512 kByte; for SC – see formula in spec(page 255).

RCA (relative card address) – 16bits, see CMD3

DSR (driver state register) – optional(see CSD reg. above), config. interface, see CMD4.

SCR (SD Card configuration register) – read-only(via ACMD51), almost useless, except
- SD_BUS_WIDTHS – what bus widths are supported
- SD_SPEC – Supported spec. version

CSR (card status register) – status flags, returned in R1 response, may be requested by CMD13
- COM_CRC_ERROR – CRC of command failed.
- ILLEGAL_COMMAND – not defined or not applicable in current state.
- READY_FOR_DATA – can card accept next data block or prev. is still not programmed.

SSR(SD Status) – 512bits, sent to host via DATx. Contains even more info about card. Request by ACMD13.
## Useful commands
stuff bits and reserved bit – just set 0

### CMD0 - reset

### CMD8
Helps to define card’s version, enables more functions for hight-capacity and extended-capacity cards. Just use it during identification.

Arguments

### CMD55 – next CMDx is ACMDx
Makes next command an application specific(ACMDx).

### ACMD41
Send VDD window, card which does not support this range – go to idle(and do not respond).
Also may just request supported window(see below).
Also checks, that card’s initialization is complete – “busy” in response(but not longer, than 1sec).

Arguments

Just set XPC=0 (card will operate at default speed 12MHz?? and consume 100mA). You will not reinitialize to use other speed class.
Set HCS=1 for HC or XC card – otherwise it will never complete initialization(will always be busy).

Note: response R3 does not contain valid CRC.
Note: argument has extra bit HO2T - indicates, that host supports UC card. If not set – UC card will never complete initialization(as HC with HCS=1). OCR also has extra bit CO2T.

Response

Card capacity status(CCS) is response is valid after init. completed.

### CMD2 – get card ID
Request “Card ID”(CID)

### CMD3 – get relative address
Requests “Relative card address”(RCA) – card will be further addressed by this.
Host may request RCA many times(if prev. are not suitable) – last received is active.

### ACMD42 - disable pull-up on DAT3
Disable pull-up resistor on DAT3(card detection pin).

### CMD13 - request card status

### ACMD13 – request SD status

### CMD4 - conf. driver stage.(write DSR register)

### CMD9 - request CSD register
Request “card specific data”: block length, storage cap., etc.

### CMD7 - put card in “transfer state”(tran, see “data transfer mode” state diagram above)

### CMD16 - set block length.
Applicable only for SC cards and only if you want to use “partial block writes”. Does not have effect for HC, XC cards - block is always 512bytes.

### ACMD6 - change width of data-bus

### CMD17 / 18 - read single / multiple block.

### CMD12 - stop read / write

### CMD24 / 25 – write single / multiple block

# CAN
CAN has active pull-up on TX pin during sleep mode??
Modes: sleep(low power, all stopped but you may access mailboxes), initialization(to reconfigure peripheral) and normal.
Transition between modes is requested by CAN_MCR.INRQ(init. mode request) and CAN_MCR.SLEEP(sleep mode request). CAN_MSR.INAK/SLAK – confirm the end of transition. For normal mode – clear both INRQ and SLEEP and wait for both INAK and SLAK to be cleared.
Change only in init. mode: bit-rate (CAN_BTR), options in CAN_MCR.
Input filter configuration does not depend on init. mode BUT filter’s scale and mode should be configured prior entering normal mode i.e. during sleep or init. mode.
Any filter’s config. should be done when filter is not active – FACTx = 0
When FINIT=1, CAN reception is deactivated?? Is FACTx – responsible for filter-bank???
To initialize the registers associated with the CAN filter banks (mode, scale, FIFO
assignment, activation and filter values), software has to set the FINIT bit (CAN_FMR)
In sleep mode CAN may monitor the bus and wake up + generate IRQ on activity.

# CMSIS-DSP
MVE-functions – rely on Cortex-M Vector Extension Unit(it is hardware).

Python wrapper
Generate docs using Sphinx: pip install sphinx
C-functions which return arm_status → functions which return (arm_status, result)
Provide FIR coefficients in reverse order.

Static lib compilation
add_compile_definitions(__FPU_PRESENT=1)

Useful notes
arm_conv_partial_...(…, float32_t pDst, uint32_t firstIndex, …) - result appear from pDst[firstIndex]
arm_atan2_...() - in “Fast Math Functions”, phase of complex number.

FIR filters
Process samples in blocks. Provide coeff. in reverse order.
Size of state buffer: {num. of filt. coeff.} + {sample block size} - 1

IIR filters
Coeff. of single stage are stored as: {3 for numerator}, {2 for denom. - don’t put first “1.0”}
Negate coefficients for denominator.
Biquad., direct form 1. State buffer len.: 4 * {num. of stages}
Biquad., direct form 2, transposed. State buffer len.: 2 * {num. of stages}

sin/cos
arm_sin_cos_...() - in “Controller Function”, calcs. both sin and cos, accept degrees.
arm_sin_...()/arm_cos_...() - in “Fast Math Functions”.