ChibiOS/RT – fully featured OS
ChibiOS/NIL – OS version for tiny devices
ChibiOS/HAL – high-level periph. drivers
OSAL – used by HAL to abstract from RTOS; synchronization, interrupts, time management, run-time errors, etc.

chconf.h – config scheduling, memory management, enable features(mutexes, queues)
halconf.h – enable periph. drivers and config them(default baud-rate, size of buffer)
mcuconf.h – MCU specific configs(clock dividers, interrupt priorities, DMA streams assignment)

static THD_WORKING_AREA(waThread1, 128);
static THD_FUNCTION(Thread1, arg) {… } - macro to create thread-function, why need?

#include "ch.h"
#include "hal.h"

At the beginning of main()
halInit();
this makes main() function to become a thread with NORMALPRIO priority
it also creates idle thread with IDLEPRIO priority??
chSysInit();

Higher priority threads have greater priority number.

Memory Heap allocates memory of any size, memory pool – allocates memory of fixed size.

Creating a thread – starts it immediately(no need to start scheduler like in FreeRTOS)
chThdCreateStatic(...)
chThdCreateFromHeap(...)
chThdCreateFromMemoryPool(…)

chThdSleepMilliseconds()

# Create project
Should be make-project. CMake does not allow to include make-files.
Copy makefile from demo projects and edit it.

Notes about makefile content:
$(CHIBIOS)/os/common/startup/ARMCMx/compilers/GCC/mk/startup_stm32f7xx.mk – defines several shared variables with paths; includes CMSIS and header with MCU-specific defines(stm32f756xx.h) – all is supplied with chibi.
Still allows to use custom linker-script – that is why .ld-file is specified separately. You may use __main_stack_size__ and __process_stack_size__ variables in your custom .ld-file. They will be substituted by USE_EXCEPTIONS_STACKSIZE and USE_PROCESS_STACKSIZE values.
$(CHIBIOS)/tools/mk/autobuild.mk – builds lists of sources(.s, .c, .cpp); by default starts scanning from ./source - change this by defining variable AUTOBUILD_ROOT; all subdirs of AUTOBUILD_ROOT are added as include dirs.
$(CHIBIOS)/os/common/startup/ARMCMx/compilers/GCC/mk/arm-none-eabi.mk – correct name of GCC tools.
$(CHIBIOS)/os/common/startup/ARMCMx/compilers/GCC/mk/rules.mk – contains targets and instructions to build.

board.h/c files:
board.h – MCU type(like STM32F756xx) voltage level, clock related defines, void boardInit(void) declaration but inside
#if !defined(_FROM_ASM_)
#endif
All required defines are listed in hal_lld.h(see below)

board.c – implement boardInit(void).

Definitions for mcuconf.h and board.h
List of all defines are in os\hal\ports\STM32\STM32F7xx\hal_lld.h
Note: may include header for specific MCU.

# Notes about ChibiOS file structure
All related to chibi in os/
os/common/ports/ - ports related to MCU core
os/hal/ports/ - ports related to MCU peripherals
os/hal/ports/STM32/STM32F7xx – mainly defines and impl. of clock-tree configuration
os/hal/ports/STM32/LLD – impl. of periph. drivers.
What about test/ and testex/?

# PAL Driver(GPIOs)
PAL - Port Abstraction Layer
It’s enough to include “hal.h”.

It’s more platform independent to use IOPORT1/2/… instead of GPIOA/B/…, but 1st is just an alias, like:
#define IOPORT1	GPIOA

Line – “packs” port and pin in 1 variable:
#define LINE_LED_RED	PAL_LINE(GPIOA, 0U)
Naming convention:
- palSetPad(GPIOA, 0U) – API with “Pad” takes port & pin
- palSetLine(LINE_LED_RED) – API with “Line” takes just line

## Pin configuration
palSetPadMode(GPIOA, 0,
PAL_MODE_OUTPUT_PUSHPULL | PAL_STM32_OSPEED_HIGHEST)
mode-arg(3rd). is a bit-field, allows to combine platform independent PAL_MODE_… and MCU specific PAL_STM32_… config-flags.

PAL_MODE_UNCONNECTED – special standard mode for unconnected pins, may be pulled-up input or analog input – this is MCU dependent.

PAL_MODE_ALTERNATE(5) – macro to specify alternative function mapping:
palSetPadMode(GPIOA, 0,
PAL_MODE_ALTERNATE(5) | PAL_MODE_OUTPUT_OPENDRAIN)

Configure several pins of port at once:
palSetGroupMode(GPIOA, mask, offset, mode)
Affected pins are defined by (mask<<offset):
palSetGroupMode(GPIOA, 0x01, 0, mode) – configures PA0
palSetGroupMode(GPIOA, 0x01, 4, mode) – configures PA4
PAL_PORT_BIT(0) – helper macro to create mask, pass offset=0; configure PA0 and PA4:
palSetGroupMode(GPIOA, PAL_PORT_BIT(0) | PAL_PORT_BIT(4), 0, mode)
mode – bit-field as above.

## Writing to port
palSet...(…) - sets(to 1) pad/line/port pins
palSetPad(GPIOA, 0)
palSetLine(LINE_LED_RED)
palSetPort(GPIOA, PAL_PORT_BIT(0) | PAL_PORT_BIT(1))
palClear...(...) - clears(to 0) pad/line/port pins
palWrite...(…) - writes specified value to pad/line/group/port pins
palWriteGroup(GPIOA, PAL_PORT_BIT(0), 0, 0x03) // PA1 stays unchanged because of mask
palToggle...(…) -

## Reading port
palRead..() - reads pad/line/group/port. WTF is palReadGroupLatch()??
palReadPad/Line() returns PAL_LOW or PAL_HIGH