cmake_minimum_required(VERSION 3.10)
Version may be a range: VERSION 3.1...3.15

project(MyProject VERSION 1.0
        DESCRIPTION "Very nice project"
        LANGUAGES CXX)
This also creates vars. MyProject_VERSION and PROJECT_VERSION. PROJECT_NAME will be set “MyProject”. Mandatory is only 1-st arg.(MyProject).

# Local variables
set(VAR_NAME “value”) – defining local variables
option(VAR_NAME “ON”) – defining boolean local var.
${VAR_NAME} or “${VAR_NAME}”– getting value. “” are not mandatory, but VAR_NAME should NOT contain spaces. So “” ensure that everything will work even with spaces
set(ENV{variable_name} value) and get $ENV{variable_name} – accessing environment variables

# Properties
Similar to local vars., but are “attached” to some target.
Many target properties are initialized from a matching variable with CMAKE_???

set_target_properties(TargetName PROPERTIES CXX_STANDARD 11)
set_property(TARGET TargetName PROPERTY CXX_STANDARD 11)

get_target_property(ResultVariable TargetName PropertyName)
get_property(ResultVariable TARGET TargetName PROPERTY PropertyName)

# Useful local vars. and props.
CMAKE_SYSTEM_NAME – For what OS to build: Generic(unknown, embedded system)/Linux/Android/Windows. By default is set to CMAKE_HOST_SYSTEM_NAME. Read manual if use cmake from MSYS2 or Cygwin.
PROJECT_BINARY_DIR – path to build dir.
CMAKE_SOURCE_DIR – path from where top-most CMakeLists was “invoked”
CMAKE_CURRENT_SOURCE_DIR – where cmake is currently working; useful when added sub directory(with own CMakeLists)
INCLUDE_DIRECTORIES, INTERFACE_INCLUDE_DIRECTORIES - ;-separated lists of target’s inc. dirs. May be populated by target_include_directories(..) (see below)
STATIC_LIBRARY_OPTIONS - ;-separate list of linker options for STATIC library
INTERFACE_LINK_OPTIONS – public link-options required for a library, may be populated by target_link_options(…) - see below. Not for STATIC libraries.
LINK_OPTIONS – link options for executable or shared lib. Not for static library. See target_link_option(..) below.
INTERFACE_COMPILE_DEFINITIONS, COMPILE_DEFINITIONS – similar to above, list of defines (like #define x in code).
INTERFACE_LINK_DIRECTORIES, LINK_DIRECTORIES – similar to above, list of paths where to search libraries.
CMAKE_PREFIX_PATH – path where find_package(), find_program(), find_library(), find_file(), and find_path() will search artifacts(every may append bin, lib, include etc.).
CMAKE_LIBRARY_PATH – ;-separate list of paths where find_library(…) should search library. Should be set by project.
CMAKE_SYSTEM_LIBRARY_PATH – ;-separate list of platform specific paths where find_library(...) should search library. Do not modify it in project.
DEBUG_CONFIGURATIONS - ;-separate list of configuration names which should be treated as debug configs. Used by target_link_libraries().

# Local vars. to define toolchain
set(CMAKE_C_COMPILER arm-none-eabi-gcc)
set(CMAKE_CXX_COMPILER arm-none-eabi-g++)
set(CMAKE_ASM_COMPILER arm-none-eabi-gcc)
set(CMAKE_AR arm-none-eabi-ar)
set(CMAKE_OBJCOPY arm-none-eabi-objcopy)
set(CMAKE_OBJDUMP arm-none-eabi-objdump)
set(SIZE arm-none-eabi-size)
set(CMAKE_TRY_COMPILE_TARGET_TYPE STATIC_LIBRARY) – important for cross-compilation

# Generator expression($<KEYWORD:value>)
Ha 2 forms: $<KEYWORD> and $<KEYWORD:value>. Are evaluated at “build“ or “install” time – this is their advantage over local vars. and target’s props.
In 1st form KEYWORD is substituted by actual value – works like props. But even during “install”.
In 2nd form semantics are:
1) if KEYWORD like True → return value.
2) if KEYWORD == value → return true, example of adding a flag but only for Debug:
target_compile_options(MyTarget PRIVATE "$<$<CONFIG:Debug>:--my-flag>")
3) KEYWORK – operation, value argument(or ,-separated list). Example:
$<EQUAL:${x},${y}> - returns True if x == y.
## Useful examples
Use different include dirs. for building and after installation.
target_include_directories(my_library PUBLIC
$<BUILD_INTERFACE:${CMAKE_CURRENT_SOURCE_DIR}/include>
$<INSTALL_INTERFACE:include>)
# Useful commands
add_executable(one two.cpp three.h)
add_library(one STATIC two.cpp three.h) – or STATIC, SHARED, MODULE

add_subdirectory(source_dir [binary_dir] [EXCLUDE_FROM_ALL] [SYSTEM]) – add dir. with it’s own CMakeLists.txt and sources to the build. binary_dir – path(relative to build dir. or absolute) where to build this sub. dir. EXCLUDE_FROM_ALL excludes targets from sub. dir. from ALL targets of parent CMakeLists – this subdir should be build separately.

target_include_directories(target_1 PUBLIC inc)
- PUBLIC – “inc” will be visible to dependent targets(projects)
- PRIVATE – “inc” is visible only to target_1
- INTERFACE – only needed for dependent target. Used when building library and defining in which header API resides.
PRIVATE and PUBLIC populate INCLUDE_DIRECTORIES property of <target>. PUBLIC and INTERFACE – INTERFACE_INCLUDE_DIRECTORIES.
include_directories(inc) – “inc” will be visible to all targets in current CMakeLists and added(below this statement) sub directories.

target_sources(<target> <INTERFACE|PUBLIC|PRIVATE> [items1...]
<INTERFACE|PUBLIC|PRIVATE> [items2...] …) - what is this??

target_compile_definitions(<target> <INTERFACE|PUBLIC|PRIVATE> x y=1
<INTERFACE|PUBLIC|PRIVATE> [items2...] …) - like #define x in code, adds -D arguments to compiler command line. PRIVATE and PUBLIC populate property COMPILE_DEFINITIONS, PUBLIC and INTERFACE - INTERFACE_COMPILE_DEFINITIONS
add_compile_definitions(ARM_MATH_CM4 ARM_MATH_MATRIX_CHECK)
add_definitions(-DSTM32 -DSTM32F1) – do not use this, it is legacy

target_compile_options(MyTarget PRIVATE "$<$<CONFIG:Debug>:--my-flag>")
add_compile_options(-mcpu=cortex-m3 -mthumb)

target_link_options(<target> [BEFORE] <INTERFACE|PUBLIC|PRIVATE> [items1…] [<INTERFACE|PUBLIC|PRIVATE> [items2...] …) - not for STATIC library, use set_target_property(STATIC_LIBRARY_OPTIONS, …) instead. BEFORE means prepend(not append) new options. PRIVATE and PUBLIC populate LINK_OPTIONS, PUBLIC and INTERFACE – INTERFACE_LINK_OPTIONS.
add_link_options(-mcpu=cortex-m3 -mthumb)

target_link_directories(<target> [BEFORE] <INTERFACE|PUBLIC|PRIVATE> [items1...]
<INTERFACE|PUBLIC|PRIVATE> [items2...] …) - absolute or relative paths where to search libraries. Populate properties INTERFACE_LINK_DIRECTORIES and LINK_DIRECTORIES.
link_directories([AFTER|BEFORE] directory1 [directory2 ...])

find_library(var_to_store libname [path1 path2 …]) - search library “libname” in specified paths or CMAKE_LIBRARY_PATH, CMAKE_SYSTEM_LIBRARY_PATH, CMAKE_PREFIX_PATH variables.

target_link_libraries(MyTarget item1 item2 …) - spec. what libraries to use while linking. Each item may be: target name(defined in this CMakeLists), full path or just name of a library(even without extension).
link_libraries(...)

find_package(???)

install(TARGET TargetName PUBLIC_HEADER) – the simplest form, resulting .exe/.lib, will be placed in “bin”/”lib” subdir. Public headers will be in “include” subdir. TargetName should have property PUBLIC_HEADER with a list of public headers.

file(...) - search/read/write/convert/etc. files and dirs.
1) List files/dirs. which match globbing expression (with *, ? wildcards):
 file({GLOB or GLOB_RECURSE} ResultVar [LIST_DIRECTORIES true|false] [RELATIVE <path>] [CONFIGURE_DEPENDS] <globbing-expressions>…)
LIST_DIRECTORIES – default true for GLOB, default false for GLOB_RECURSE
GLOB_RECURSE – go recursively deeper, has no-value opt. flag FOLLOW_SYMLINKS.
RELATIVE <path> - results will be “relativised” to <path>.
CONFIGURE_DEPENDS – flag which trigger re-list files before build. This was invented not to list all sources manually. It may not work on some generators.

add_custom_command(TARGET ${PROJECT_NAME}.elf POST_BUILD
        COMMAND ${CMAKE_OBJCOPY} -Oihex $<TARGET_FILE:${PROJECT_NAME}.elf> ${HEX_FILE}

# Generating script for build tool
Generate inputs for make(or other build tool). Here I define path to sources(actually folder with CMakeLists.txt, sources are defined there) and build dir.

cmake -S ./src -B ./build

Choose desired tool by adding -G"MinGW Makefiles"

Specify option by adding -DCMAKE_BUILD_TYPE=Debug – sets CMAKE_BUILD_TYPE=”Debug”

Other useful options:
- CMAKE_INSTALL_PREFIX – path to “install” directory
- BUILD_TESTING – “ON”/”OFF”???, some test tools use this
- CMAKE_MODULE_PATH - ; separated paths (with /) where to search cmake modules(for include() or find_package()). No need to spec. path to default modules, if no custom modules – it is “”.

# Building
cmake --build ./build
VS toolchain allow “--config Debug” option to define configuration right before building. Other may require build type(see above) for generation phase.

# Installing
cmake --install ./build --prefix