# KiCad
How to set 1-layer PCB?
## BOM generation
In schematic editor: Tools → Generate BOM
Most convenient BOM generator script is “bom_csv_grouped_extra”.
## Symbol editor
“Pin name” set to “~{EN}” appears as inverted EN.
“Pin name” set to “~” is equivalent to empty name.
## Layers
Edge.Cuts – physwical outline of a board. Some manufacturers want internal cutouts in this layer.
Margin – some technical layer, does not have specific purpose. DRC does not check anything about it. Makes sense to use it for outlines of components.
## Routing hints
Change track width “on fly” – Q
Add via during routing - V

# LTSpice
1m – 1 milli, 1Meg – 1 mega.
## Hot keys
Rotate: Ctrl+R
Mirror: Ctrl+E
View simulation logs(with calculated outputs): Ctrl+L
## Import custom model
## Useful directives
Define parameter:
.param my_param 1u
Use parameter as value for component(like resistance for resistor) – set “Value” to “{my_param}”.

Run operating point analysis:
.op

DC sweep:
.dc V1 0 2 1
to sweep source designated as V1 from 0 to 2 and inc. by 1 on each step.
.dc V1 list 0 1 2
to use values from the list.
.dc param my_param 0 2 1 – will work??
.DC temp -10 80 100m
temp. sweep.
Sweep parameter(any configured simulation will be repeated with different values of “my_param”):
.step param my_param 0 2 1
.step param my_param list 0 1, 2

.probe alli - ngspice directive that enables measurement and handling of all currents, a feature not present by default – will work??

plot V(out)*I(R2)+V(N002)*I(R1) – will work??
## sw - voltage controlled switch
Set property “Value” to “MYSW”, write directive:
.model PWR_SW SW(Ron=0.5 Roff=100Meg Vt=0.5 Vh=0.1)
where Ron/Roff – close/open resistance; Vt – threshold; Vh – hysteresis(actual thresholds Vt +/- Vh, not Vt +/- Vh/2). If Vh < 0 – switch changes resistance smoothly between Vt +/- Vh.
## e, e2 - voltage controlled voltage source
e2 is like e, but with vertically mirrored inputs.
To limit output voltage to 3.5V set prop. “Value” to:
table=(-1u, 0, 1u, 3.5)
where -1u, 0 and 1u, 3.5 – are “input, output” pairs. There might be more pairs. If input signal is between 2 input values from table – output signal is interpolation of corresponting output values from table.
g – voltage controlled current source
https://www.analog.com/en/resources/technical-articles/ltspice-simple-steps-to-import-third-party-models.html
PWL()
FIND WHEN …
https://ieee.li/pdf/viewgraphs/ltspice_creating_a_schematic_symbol.pdf