# USB type C
https://www.usb.org/sites/default/files/USB%20Type-C%20Spec%20R2.0%20-%20August%202019.pdf
Type-C is spec. for connector, it is independent from USB 3.1 Gen1/2 and Power Delivery features. Actually DisplayPort(for video like HDMI but newer) and Thunderbolt(multiplexed PCIe and DisplayPort) technologies use type-c as connector.

USB-PD is protocol, which enables 100W power supply delivery.

DFP(downstream facing port) – name of a port on host. USB-PD DFP may either source supply(to devices) or consume supply(from charger).

UFP(upstream facing port) – name of a port on device.