# USB type C
https://www.usb.org/sites/default/files/USB%20Type-C%20Spec%20R2.0%20-%20August%202019.pdf
Type-C is spec. for connector, it is independent from USB 3.1 Gen1/2 and Power Delivery features. Actually DisplayPort(for video like HDMI but newer) and Thunderbolt(multiplexed PCIe and DisplayPort) technologies use type-c as connector.

USB-PD is protocol, which enables 100W power supply delivery.

DFP(downstream facing port) – name of a port on host. USB-PD DFP may either source supply(to devices) or consume supply(from charger).

UFP(upstream facing port) – name of a port on device.

# TVS Diodes
“Reverse stand-off voltage” is the same as “reverse working voltage”(VRWM) — device does not leak much current(~10nA) at this voltage.
Breakdown voltage – device conducts visible current(~1mA) at this voltage.
Clamping voltage – max. voltage during shock.

Devices in SOT-143 mainly contain this:

# 74xx logic series
Table: https://en.wikipedia.org/wiki/7400-series_integrated_circuits

# SSDs
SATA – interface.
SCSI – set of standars for connectors, electrical signals, …, protocols.
AHCI – protocol for SATA drives.
NVMe – protocol for solid-state drives.

PCIe – serial interface, replaced parralel PCI. PCIe may have 1 or several lanes(2 diff. pairs for full duplex communication). PCIe x1 – has 1 lane, PCIe x4 – has 4 lanes. Don’t confuse interface version(3.0 or 4.0) with number of lanes: PCIe 3.0 x4 – ver. 3.0 with 4 lanes.

M.2 – form factor & connector of SSD. Actually PCIe or SATA or USB buses may be connected to pins of M.2 connector.
Form factor presumes several sizes of module: M.2 2230 – 22mm width and 30mm length; M.2 2280 – 22mm width and 80mm length; etc.
Also psesumes several variants of connector keys(notches which guaranty correct connection):
B key - supports SATA, PCIe x1, PCIe x2; M key - supports PCIe x2, PCIe x4 (NVMe); B+M key - Dual Key, supports SATA and PCIe x1/x2 (common for SATA M.2 SSDs).